## Slide 1: Displays: requirements
Resolution
Contrast
Brightness
Color rendition
Speed
Power consumption
Cost
Ruggedness
UV tolerance
Special features (3D, touch, swipe)

## Slide 2: (Backlit) LCD: the common workhorse
Rotates polarisation angle of light falling through 2 perpendiculary polarized plates
Backlight: blue led with yellow phosphor give white impression, diffuser plate
Medium power consumption
(Still) limited view angle
Still a bit slow
Polarizing filter
“Per pixel” electrode
Liquid crystals rotate pol. angle
Common electrode
Polarizing filter, perpendic. to 1
Backlight or reflector

## Slide 3: CRT: speed and vector graphics
Mass market declining
Niche markets:
  High color fidelity (professional photography and video)
  Wide view angle
  High speed
  High contrast
  High resolutin
  Vector displays
  Light guns / light pens
  Relatively low power consumption compared to high-end LCD
  Can stand extreme cold and heath

## Slide 4: Plasma: very high contrast and speed
Cells filled with ionized gas (plasma), like TL lamp
Very high contrast, deep blacks
High speed
Wider view angle than LCD
Powerconsumption comparable to CRT
Prone to burn in and aging
Economically attractive for screendiag. > 80 cm
Good color rendition
Competed by LED

## Slide 5: Electronic paper: low power, high contrast, readable in direct daylight
No back lighting, works with environment light, so intrinsically adaptive and low power
Can hold static text without any power consumption
Better contrast that ordinary newspaper
May be flexible (roll up)
Slow
Color just becoming available

## Slide 6: Beamers: brightness and longevity?
Mostly use LCD’s with light falling through from a conventional lightbulb (longevity?)
LED’s and laser diodes on the rise
Used for smart boards, home cinema’s, promotional purposes, meeting room displays
Pico-projectors on the rise (connect to smart phone etc.)
Noise level may be important (cooling fan)
Not yet common in commercial cinema due to quality limitations, due to change

## Slide 7: LED: big, bright and expensive
140 m² no exception
Visible even in direct sunlight
About $3000/m², but quite profitable (soccer)
Special driver software
High power consumption

## Slide 8: 3D displays: Anaglyph
Cheap glasses
No special display
“Normal” colors visible after getting used to
Stereoscopic

## Slide 9: 3D displays: Polarized
Good image, no false color
Special display
Medium cost glasses
Popular (cinema)
Stereoscopic

## Slide 10: 3D displays: Shutter
Good image separation
Expensive
Stereoscopic
Interface to normal display

## Slide 11: 3D displays: Auto-stereoscopic
No glasses
Special expensive display
Limited view angle
Trend for television sets

## Slide 12: 3D displays: Holographic
The future
Not stereoscopic but true multi-angle
Very high bandwith
Very high screenresolution needed
Outdoor settings problematic
(ethane molecule model)
studio
display